***********************Draft***********************
Icarus Simulator
helloworld simulation
repo 102121icozip
10/10/23

***********************Draft***********************

The helloworld_tb.v needs to be created. See catboard-relook/doc/iverilog/helloworld_tb.v

devel@pi4-20:~ $ cd 102121icozip/rtl/uart/

devel@pi4-20:~/102121icozip/rtl/uart $ iverilog -o dsn helloworld_tb.v helloworld.v
The following
initial
begin
#1920000
$finish();
end

devel@pi4-20:~/102121icozip/rtl/uart $ vvp dsn
VCD info: dumpfile helloworld.vcd opened for output.
devel@pi4-20:~/102121icozip/rtl/uart $

devel@pi4-20:~/102121icozip/rtl/uart $ vvp dsn
VCD info: dumpfile helloworld.vcd opened for output.
Killed

devel@pi4-20:~ $ kill -9 9093

devel@pi4-20:~/102121icozip/rtl/uart $ gtkwave helloworld.vcd

GTKWave Analyzer v3.3.104 (w)1999-2020 BSI

[0] start time.
[1920000000] end time.

devel@pi4-20:~/102121icozip/rtl/uart $ gtkwave helloworld.vcd

GTKWave Analyzer v3.3.104 (w)1999-2020 BSI

Near byte 57770007, Unknown VCD identifier: '11101100101000010010'
[0] start time.
[9697700] end time.
reg	pwr_reset;
initial	pwr_reset = 1'b1;
always @(posedge i_clk)
pwr_reset <= 1'b0;

reg	[24:0]	ledctr;
initial	ledctr = 0;
always @(posedge i_clk)
if (!o_uart_tx)
ledctr <= 0;
else if (ledctr != {(25){1'b1}})
ledctr <= ledctr + 1'b1;
assign	o_ledg = !ledctr[24];

reg	[7:0]	message	[0:15];

initial begin
message[ 0] = "H";
message[ 1] = "e";
message[ 2] = "l";
message[ 3] = "l";
message[ 4] = "o";
message[ 5] = ",";
message[ 6] = " ";
message[ 7] = "W";
message[ 8] = "o";
message[ 9] = "r";
message[10] = "l";
message[11] = "d";
message[12] = "!";
message[13] = " ";
message[14] = "\r";
message[15] = "\n";
end

The above image has time where as the image below time is unknown.

i_setup is 0x364 or 868 is for a baudrate 115200.

100000000	115200	868.055555555556
100000000	230400	434.027777777778
100000000	345600	289.351851851852
100000000	460800	217.013888888889

100000000	921600	108.506944444444

100000000	1843200	54.2534722222222

In the image below the baud rate would be increased 1M.
15 characters transmitted in 81400ns.

Xx
In the image below the baud rate would be increased 4M.
15 characters transmitted in 21300ns.

xx
state is 0-9 for the 10 bits to transmit 1 ASCII chacter.

devel@pi4-20:~/102121icozip/rtl/uart $ git diff helloworld.pcf
diff --git a/rtl/uart/helloworld.pcf b/rtl/uart/helloworld.pcf
index 8337466..b12f38f 100644
--- a/rtl/uart/helloworld.pcf
+++ b/rtl/uart/helloworld.pcf
@@ -13,6 +13,6 @@ set_io o_ledg A9 #IOT_194 LED1
 #set_io o_ledr B7 #IOT_207 LED4

 set_io i_rts A1 #IOT_220 PM2-A1 i_rts
-set_io o_uart_tx B3 #IOT_214 PM2-A3
-set_io i_uart_rx B5 #IOT_223 PM2-A2
+set_io o_uart_tx B3 #IOT_214 PM2-A2
+set_io i_uart_rx B5 #IOT_223 PM2-A3
 set_io o_cts B6 #IOT_208 PM2-A4 o_cts